## Slide 1
Water quality in Berambadi
Buvaneshwari S (PhD student)
J. Riotte, L. Ruiz, Sekhar M., Mohan Kumar M.S.

## Slide 2
1- What is the status of groundwater quality in Berambadi ?
= link with GW resource, land use practices ?
= possible issues, positive aspects for crop yield ?
= influence of soil type ?
2- Fate of nutrients at soil-plant scale ?
= Providing N data for STICS calibration
Monitoring spatial variability of groundwater chemistry (n=160)
(supported by environmental observatory BVET), comparison with resource
N and Cl mass balance at soil-plant scale : influence of soil on recharge and N leaching
Objectives

## Slide 3
Deep GW levels, many borewells failed in this region
Annual N application in watershed ≈ 12 tons N/km2
Application in irrigated area = 2 x rainfed area
(ppm)
Buvaneshwari et al., in press STOTEN
Spatial variations of NO3 in Berambadi groundwater

## Slide 4
1D governed by local practices => solute recycling
2D controlled by the Lateral groundwater flow
1D- Solute recycling
2D- Lateral flow
Groundwater gradient (%)
Buvaneshwari et al., in press STOTEN
Groundwater flow and NO3

## Slide 5
Extreme nitrate :
+ Deep GW
+ Very Low gradient
+ Very low discharge
= Severely depleted water resource
50
100
200
360
NO3 (mg/L)
Groundwater status and NO3
Low to moderate NO3 =
High gradient + high discharge and/or
Shallow GW (= Potential water resource)
Buvaneshwari et al., in press STOTEN

## Slide 6
Vulnerability to salinization : Chlorine in groundwater
Buvaneshwari et al., in prep.
Hot spots of Cl spread in the watershed

## Slide 7
Controls of Cl in groundwater
Buvaneshwari et al., in prep.
Compared to nearby forest groundwater,
= highest evapotranspiration + evidence of KCl impact

## Slide 8
Total GW chloride
Soil texture
Chloride natural
Chloride excess
mg Cl /L
Chloride excess due to KCl application explains hot spots
Hot spots = up to 95 % of Cl originates from fertilizer (highest in GW depleted areas)
Highest natural chloride located in lowland = Vertisols areas (higher evapotranspiration)
30
30 - 45
45 - 70
70 - 100
Deconvolution natural vs anthropogenic chloride
Buvaneshwari et al., in prep.
100 - 140
> 140

## Slide 9
Soil-plant scale solute budget : monitoring set up
Profile of rhizon samplers
TDR tube
above root zone (soil input, 10cm)
below root zone (soil output, 100cm)
Root zone
Soil moisture profile
Soil solution composition
Water input (irrigation, rainfall)
Rain gauge
LAI
Monitoring
Turmeric + barren soil
Vertisol + Ferralsol
Sampling frequency: every 15 days
= 40 Soil pore water and 60 soil samples per month
Fertilizer input

## Slide 10
FCl input
(gCl /m2)
16
Rain = 0.7
Fertilizer
300mm
15
9.5
63 250mm
Irrigation
Vertisol
Ferralsol
[Cl]output 90 mg/L 370 mg/L
Estimated recharge : 280 mm/yr 210 mm/yr
Cl from rain negligible in the balance
Cl from fertilizer and irrigation higher in Vertisol than Ferralsol
Recharge in Ferralsol > in Vertisol
First assessment of chlorine mass balance (turmeric crop)

## Slide 11
FN input
(gN /m2)
Vertisol
Ferralsol
Irrigation
Rain = 1
Fertilizer
2.5 (250mm)
35
25
7 (300mm)
≈ 30 gN /m2
≈ 2-10 gN /m2
N flushed down in Ferralsols
N consumed efficiently in Vertisols… but risk of salinization
N by irrigation = potentially important source than should be taken into account by farmers
Simplified N mass balance in Ferralsols and Vertisols (turmeric crop)
NO3 leaching :

## Slide 12
Watershed scale :
Monthly monitoring of groundwater levels (n=200) available
Bi-annual monitoring of GW composition, 2012-15 (n= 160) available
=> Links between extreme NO3 and GW depletion areas
=> “hidden” NO3 flux due to irrigation up to 200 kgN/ha/yr
=> Cl impacted by both fertilizer (KCl) application and relative evapotranspiration
Soil-plant scale :
Bi-monthly monitoring of soil pore water composition (turmeric, bare soil) available
=> role of soil type on water and nutrient balance
Perspectives
“hidden” NO3 flux due to GW irrigation up to 200 kgN/ha/yr needs to be taken into account in fertilization plan
Risk of salinization
Need to improve nutrient balance at soil-plant scale (gas component, crop diversity)
Conclusions & perspectives

## Slide 13
Thank you

## Slide 14
Assumption : Cl conservative
Steady state (Clinput = Cloutput) at yearly scale
No stock variation within soil
Plant uptake neglected
FCl soil input
FCl soil output
Soil
Fertilizer (KCl)
GW irrigation
Rainfall
Estimation of local recharge with chlorine mass balance

## Slide 15
Nitrate (mg NO3/l)
Ferralsol
Vertisol
Depth
(cm)
High, stable NO3
lower, variable NO3 (peak diffusion)
Profiles of NO3 in soil pore water, turmeric crop